| Speed: max. 65 strokes/ minute | Air consumption: ca. 10Nm³/ h |
| --- | --- |
| Output: max. 300 blister/ minute | Operating pressure: 6-7bar |
| Sealing/ Forming dimensions (Format plate): | Cooling water: 0.12 m³/h |
| diagonally max. 150 mm |  |
| longitudinal max. 175 mm | Power consumption: 11 kW |
| forming depth: max. 12 mm |  |
|  | Weight: 1600 kg |
| Forming foil dimensions: |  |
| Material: PVC, PVDC |  |
| Width: max. 160mm |  |
| Thickness:0.25mm to 0.4mm |  |
| Roll diameter: max. 450mm |  |
| Minor diameter: 70mm to 76mm |  |
| Lidding film dimensions: |  |
| Material: Alu and alu combinations |  |
| Thickness: 20 µm to 40µm |  |
| Roll diameter: max. 250mm |  |
| Minor diameter: 70mm to 76mm |  |

| Format tools BP 300/ 31 35598 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Design | Amount Blisters/ stroke | Blister-Size (mm) | Tablets/ Blister | Forming depth (mm) | Foil width Formin foil (mm) | Foil width lidding film (mm) | Material |
| 1 |  | 1x5 | 33 x 126 | 21 | 3 | 144 | 136 | Alu/ PVC |
| 2 |  |  | 36x126 | 28 | 3 | 138 | 136 | Alu/ PVC |
| 3 |  |  | 33 x 137 | 21 | 3 | 154 | 147 | Alu/ PVC |